	- Headsail -	7001125 Trevor
H0	Sail Layout	Not Yet Posted
H1	Size of Headsail (110, 135, 150 etc.)"	Staysail + Blue Water Specs	HELP
H2	Luff Length, Max Hoist, B measurement	9.00m NET webbing loop tip to webbing loop tip (Max)	HELP
H3	Leech Length	8.10m	HELP
H4	Foot Length	3.50m	HELP
H5	Tack and Head Fittings	Webbing Loops
H6	Clew Type (Press ring or 0-Ring)	O ring	HELP
H7	Leech Line	Yes
H8	Reefs for Hank on Sail (specify Qty of tiedowns)	No Manual Reefs
H9	Foot Line	Yes
H10	Track 1 (Tack to Genoa Track Beginning)	N/A	HELP
H11	Track 2 (Tack to Genoa Track Ending)	N/A	HELP
H12	Vessel "I2" Measurement	14.60m	HELP
H13	Vessel "J2" Measurement	3.79m	HELP
H14	Calculated Forestay Length	Sailmaker
H15	Reef	N/A
H16	LP	Sailmaker	HELP
H17	Color of Suncover	Canvas white	HELP
H18	Side of Sail for Suncover (port or Stbd)	Port
H19	Luff Tape Size (such as #6)	#6 (5.5mm)	HELP
H20	Furler Manufacturer	Profurl C320
H21	Foam Luff	Yes	HELP
H22	Cut Type	Cross
H23	Sail Area	Sailmaker
H24	Telltails	Yes	HELP
H25	Telltail Window	No
H26	Triple Stitch	YES
H27	Logo	No	HELP
H28	Cloth Weight	7.88oz Fastnet
H29	Sail Numbers and Color (red, blue or black)	No	HELP
H30	Sheeting Stripe (red, blue, black)	No	HELP
H31	Draft Stripe Color (red, blue or black)	Yes (Black)	HELP
H32	Clew Height off Deck	sailmaker	HELP
H33	Tack Height off Deck	525mm	HELP
H34	Luff tape starts 470mm up from Tack	470mm	HELP
H35	Specialty Sail	No	HELP
	Customer Note: All details we can check as sailmakers are based on accurate vessel I and J Measurements		HELP